## Slide 1: Characterization of Thermal Conductivity using Deterministic Phonon Transport in Rattlesnake
Jackson R. Harter
ANS Professional Conference
San Antonio, Texas
June 11 2015

## Slide 2: Outline
Background
Goals and Objectives
Methods
Test Problem
Results
Conclusion

## Slide 3: Background
Why do we care about phonon transport?
  Phonons are dominant mechanism for heat transport in ceramic based materials
  We can use information from Boltzmann transport calculations to determine thermal conductivity
      Heat flux, temperature gradient
  High fidelity simulations with deterministic solver
  Very applicable to existing and future nuclear fleet
      Real time data for thermal conductivity

## Slide 4: Background
Thermal conductivity in nuclear fuel is obtained experimentally
  Measurements on microstructure
      Analysis of fuel in different stages of burnup yields empirically fit equations (akin to thermal hydraulics correlations…)
An extremely important parameter for safe operation of a nuclear facility
  Dependent upon and influenced by many other properties, e.g. fuel and moderator temperature, isotopic concentrations

## Slide 5: Goals and Objectives
Create a module within MOOSE which uses Rattlesnake to model 3D phonon transport
      First principles, physics-based calculation
      Bridge the gap between molecular dynamics and engineering scale simulations
Characterize bulk, heterogeneous nuclear fuels with fission product defects
      UO2, PuO2
      Phonon intensity, heat flux, temperature, thermal conductivity
Adviser: Dr. Todd Palmer

## Slide 6: Methods
What is MOOSE?
  Multi-physics Object Oriented Simulation Environment
  Sophisticated framework for solving coupled PDEs
  Massively parallelizable
  Finite element mesh discretization
What is Rattlesnake?
  Solves the Boltzmann transport equation (BTE) for neutrons using the Self-Adjoint Angular Flux (SAAF) formulation
  SN and PN angular discretization, acceleration

## Slide 7: Methods
Solve the BTE for phonons
  Similar physics to radiative heat transfer
  Phonon mean free path
      Relaxation time and group velocity
      Substituted for macroscopic interaction cross section
      Scattering kernel involves equilibrium phonon distribution [Bose-Einstein, f0(ω,T)]
Deterministic numerical approach
  SN angular discretization
  Finite element spatial discretization
  Potential for multigroup treatment of phonon frequency

## Slide 8: Methods
Self-Adjoint Angular Flux formulation of BTE for phonons
Yields frequency independent, gray medium Equation of Phonon Radiative Transport

## Slide 9: Test Problem
Developed 1D code in Matlab
  1D, slab geometry, gray (frequency independent)
  SAAF transport with finite difference discretization of Morel and McGhee
    Source iteration (no acceleration for iteration on “scattering source”)
  Test problem: Si thin film calculation of temperature, heat flux, and thermal conductivity
    Yilbas and Bin Mansoor (2012)
    Si film
      3 mean free paths thick, highly scattering
      K = 157 [W·m-1·K-1]
      Cv = 1.65·106 [J·m-3·K-1]
      vg = 8430 [m·s-1]
      TL = 301 [K], TR = 300 [K]
      Λ = 33.8·10-9 [m]

## Slide 10: Test Problem

## Slide 11: Results
Rattlesnake results also reproduce those of Yilbas and Bin Mansoor
  Isotropic scattering conditions; phonon sources in YZ planes – other boundaries reflective
  Quadrature SN = 8
  Mesh generated with Cubit
  MOOSE uses PETSc - sparse linear solver with preconditioning

## Slide 12: Results

## Slide 13: Results
Rattlesnake is able to capture 1D phonon transport physics effectively
Scale of test problem involves phonon scattering in diffuse regime
  Boundary scattering dominates
  Highly diffuse, minimally ballistic
  Coarse and fine mesh yield similar results
  Temperature distribution highly linear; good agreement with other phonon transport literature

## Slide 14: Boundary Scattering Effects

## Slide 15: 2D Heterogeneous System
2D simulation of heterogeneous material
Aluminum and silicon
  Large difference in length scales and MFPs
    3.4 x 3.4 nm square aluminum
    250 x 250 nm square silicon
    ΛSi = 33.8·10-9 [m]
    ΛAl = 2.9·10-9 [m]
  Aluminum dot at 301K, emissive source
  Silicon boundaries at 300K

## Slide 16: Results
Al/Si Transient Simulation

## Slide 17: κ in UO2 single crystal
Rattlesnake simulation in comparison against experimental data in Gofryk et al.
Depleted UO2 single crystals
  Measurements taken with Physical Property Measurement System-9, 9 T superconducting magnet
  Two and four terminal probe leads – gold plated copper, connected with silver epoxy
  Sample size - 1 x 1 x 7 mm bar, annealed in Ar-6%H2 at 850˚C
Simulation run in supercell geometry ~10mfp
  MFP obtained through thermal conductivity relationship
  Used κ from experimental data
  Equilibrium κ within 0.05%

## Slide 19: Conclusion
Rattlesnake can be used to simulate phonon transport
Goal is prediction of thermal conductivity in bulk heterogeneous nuclear fuels with fission product defects
    Currently building a UO2 matrix with Xe bubbles to simulate defect scattering

## Slide 20: Future Work
Model a “real” material (UO2 with Xe defects)
Continuation into PhD
  Construct non-export controlled phonon transport module
  Incorporate frequency dependence
      Will allow greater flexibility
  Couple with MARMOT, possibly LAMMPS (external to MOOSE family)

## Slide 21: Acknowledgements
Dr. Alex Greaney, Oregon State University
Dr. David Andersson, Los Alamos National Laboratory
This study is supported under a Department of Energy grant in conjunction with the Idaho National Laboratory and National University Consortium
Contact: harterj@onid.oregonstate.edu